## Slide 1: Deuteron- versus neutron-induced radioisotope production for medicine at IFMIF-DONES
M.E. López Melero* (PhD DONES-UGR)
F. García-Infantes (PhD n_TOF-CERN)
J. Praena (Supervisor)
F. Mota, M.I. Ortíz, I. Porras, F. Arias de Saavedra, A. Roldán
*(melopez@ugr.es)
Third DONES Users Workshop, Zagreb

## Slide 2: Index:
The rise of radiopharmaceuticals in Nuclear Medicine
Radioisotope Production at IFMIF-DONES
  Why is it necessary?
  Location of the production at DONES (d and n)
  Nuclear data needs for deuterons and neutrons
  177Lu with neutrons at Test Cell: 176Yb(d,γ)177Yb177Lu
  177Lu with deuterons at R026: 176Yb(d,x)177Lu
  First prototype of target for deuterons
Conclusions and outlook
M. Elena López Melero
Third DONES Users Workshop, Zagreb

## Slide 3: 1. The rise of radiopharmaceuticals in Nuclear Medicine
M. Elena López Melero
Third DONES Users Workshop, Zagreb
Radioisotope
Linker
Vector
Molecule
Target Molecule
Tumour Cell
Radiopharmaceutical
[89Zr]Zr-Df-LEM2/15
Diagnostic
̴85%
Therapy
IHQ image corresponding to DNA double-strand break damage as measured by γH2AX-positive cells compared to both the control group, [177Lu]Lu-DOTA-LEM2/15 single-dose and [177Lu]Lu-DOTA-LEM2/15 3-dose. https://doi.org/10.1016/j.nucmedbio.2024.108930
(99Mo; 89Zr; 18F)
(131I; 90Y)

## Slide 4: 1. The rise of radiopharmaceuticals in Nuclear Medicine
M. Elena López Melero
Linker
Target Molecule
Tumour Cell
Radiopharmaceutical
[89Zr]Zr-Df-LEM2/15
Diagnostic
̴85%
Therapy
IHQ image corresponding DNA double-strand break damage as measured by γH2AX-positive cells compared to both the control group, [177Lu]Lu-DOTA-LEM2/15 single-dose and [177Lu]Lu-DOTA-LEM2/15 3-dose.
Third DONES Users Workshop, Zagreb
Theragnostic
(99Mo; 89Zr; 18F)
177Lu !!
(131I; 90Y)
Vector
Molecule
Radioisotope

## Slide 5: Index:
The rise of radiopharmaceuticals in Nuclear Medicine
Radioisotope Production at IFMIF-DONES
  Why is it necessary?
  Location of the production at DONES (d and n)
  Nuclear data needs for deuterons and neutrons
  177Lu with neutrons at Test Cell: 176Yb(d,γ)177Yb177Lu
  177Lu with deuterons at R026: 176Yb(d,x)177Lu
  First prototype of target for deuterons
Conclusions and outlook
M. Elena López Melero
Third DONES Users Workshop, Zagreb

## Slide 6: 2. Radioisotope Production at IFMIF-DONES Why is it necessary?
M. Elena López Melero
Third DONES Users Workshop, Zagreb
According to the IAEA, more medical isotope facilities are needed to secure supply in the face of growing demand.

## Slide 7: 2. Location of the production at DONES (d and n)
M. Elena López Melero
Third DONES Users Workshop, Zagreb
Schematic view courtesy of M. Vázquez
D+ (40 MeV; 125 µA)
0.1 %
0.1
5
8.3
13.9
21.3
30.3
40 MeV
D+ (40 MeV; 125 mA)
Target Assembly
Lithium
Loop
Quench
Tank
Test Cell Floor
HFTM
̴3.3 m
4.0 m
HFTM
Samples inside RIPD
Deuteron Production
Neutron Production

## Slide 8: 2. Nuclear data needs for deuterons and neutrons
M. Elena López Melero
Third DONES Users Workshop, Zagreb
176Yb(d,x)177cumLu

## Slide 9: 2. Nuclear data needs for deuterons and neutrons
M. Elena López Melero
Third DONES Users Workshop, Zagreb
Yb foils
ARRONAX cyclotron (Nantes, France)
176Yb(d,x)177cumLu
Experimental data measured by E. López-Melero in collaboration with E. Nigron and F. Haddad. 25.8 MeV deuterons on natYb targets at 100-nA beam intensity.

## Slide 10: 2. Nuclear data needs for deuterons and neutrons
M. Elena López Melero
Third DONES Users Workshop, Zagreb
Yb foils
176Yb(n,γ)177Yb  177Lu
No resonances resolved
ARRONAX cyclotron (Nantes, France)
176Yb(d,x)177cumLu
Experimental data measured by E. López-Melero in collaboration with E. Nigron and F. Haddad. 25.8 MeV deuterons on natYb targets at 100-nA beam intensity.

## Slide 11: 2. Nuclear data needs for deuterons and neutrons
M. Elena López Melero
Third DONES Users Workshop, Zagreb
Yb foils
Experimental data measured by E. López-Melero in collaboration with E. Nigron and F. Haddad. 25.8 MeV deuterons on natYb targets at 100-nA beam intensity.
176Yb2O3
Experimental data measured by F. García-Infantes at Neutron Time-of-Flight facility (CERN) with enriched 176Yb2O3 (99,43%) sample.
ARRONAX cyclotron (Nantes, France)
n_TOF at CERN
176Yb(d,x)177cumLu
176Yb(n,γ)177Yb  177Lu

## Slide 12: 2. 177Lu with neutrons at Test Cell: 176Yb(n,γ)177Yb177Lu
M. Elena López Melero
Third DONES Users Workshop, Zagreb
Reaction | Location | Irradiation Time (days) | Activity (GBq) | Specific Activity (GBq/mg)
176Yb(n,)177Yb177Lu | Nuclear Reactor | 7 | 590 | 1.11
 | 90º RIPD |  | 1 | 2.4·10-3
 | 0º RIPD |  | 6 | 1.4·10-2
Reaction | Location | Irradiation Time (days) | Activity (GBq) | Specific Activity (GBq/mg)
 | Nuclear Reactor | 7 | 590 | 1.11
 | 90º RIPD |  | 1 | 2.4·10-3
 | 0º RIPD |  | 6 | 1.4·10-2
8 cm Behind the HFTM
Inlet of the R160 duct
90º from Target
176Yb2O3
Test Cell
HFTM
RadioIsotope Production Device (RIPD)
176Yb(n,γ)177Yb

## Slide 13: 2. 177Lu with deuterons at R026: 176Yb(d,𝑥) 177Lu
M. Elena López Melero
Third DONES Users Workshop, Zagreb
Indirect Route “Carrier free”
Direct Route “Carrier added”
176Yb
d
p
n
(12,7%)
177gLu
(6.65 days)
(1.9 hours)
177Yb
<0.0037%
n
177mLu
(160 days)
Measurements were carried out at the ARRONAX cyclotron (Nantes, France) using 25.8 MeV deuterons on natYb targets at 100-nA beam intensity, in collaboration with E. Nigron and F. Haddad.
Reaction | Location | Irradiation Time (days) | Activity (GBq) | Specific Activity (GBq/mg)
176Yb(n,)177Yb177Lu | Nuclear Reactor | 7 | 590 | 1.11
 | 90º TC |  | 1 | 2.4·10-3
176Yb(d,)177Lu | 0.1% initial beam |  | 200 | 0.13
Reaction | Location | Irradiation Time (days) | Activity (GBq) | Specific Activity (GBq/mg)
 | Nuclear Reactor | 7 | 590 | 1.11
 | 90º TC |  | 1 | 2.4·10-3
 | 0.1% initial beam |  | 200 | 0.13
Yb foils
176Yb(d,x)177cumLu

## Slide 14: 2. First prototype of target for deuterons
M. Elena López Melero
Third DONES Users Workshop, Zagreb
D+ (0.1%)
Oulet Water
Inlet Water
Deuteron
Beam (0.1%)
176YbO3
176Yb2O3 :
Φ =20 mm, t=0.6 mm

## Slide 15: 2. First prototype of target for deuterons
M. Elena López Melero
Third DONES Users Workshop, Zagreb
Flow Simulation with SolidWorks tools.
Temperature distributions:
176Yb2O3 :
Φ =20 mm, t=0.6 mm
Temperatures below melting points !
3.5 l/min Fluid Flow Rate

## Slide 16: 2. First prototype of target for deuterons
M. Elena López Melero
Third DONES Users Workshop, Zagreb
Structural Simulation with SolidWorks tools.
Stress studies:
Pre-sample cut plot
Post-sample cut plot
Von Mises stress limit 200-300 MPa for natural copper !
Active stress zone
Active stress zone

## Slide 17: Index:
The rise of radiopharmaceuticals in Nuclear Medicine
Radioisotope Production at IFMIF-DONES
  Why is it necessary?
  Location of the production at DONES (d and n)
  Nuclear data needs for deuterons and neutrons
  177Lu with neutrons at Test Cell: 176Yb(d,γ)177Yb177Lu
  177Lu with deuterons at R026: 176Yb(d,x)177Lu
  First prototype of target for deuterons
Conclusions and outlook
M. Elena López Melero
Third DONES Users Workshop, Zagreb

## Slide 18: 3. Conclusions and outlook
The prototype for the production of RI with deuterons allows the encapsulation of the sample and being the first thermal and structural controls carried out with SolidWorks passed.
Taking into account both the 0.1% initial reflection of the deuteron beam and that the activity per treatment dose with conventional radiopharmaceuticals such as [177Lu]Lu-DOTA-TATE is 7.4 GBq/dose, it would be possible to cover 6 full 177Lu treatments per week.
Production via deuterons would be competitive with conventional 177Lu production routes in nuclear reactor
M. Elena López Melero
Third DONES Users Workshop, Zagreb
Nuclear measurements have been done in order to have a better knowledge about 177Lu production yield.
IFMIF-DONES can help to reduce the problem of lack of facilities for the production of RI.

## Slide 19
Thank you for your attention.

## Slide 20: X. Optimisation of Backing design
M. Elena López Melero
Third DONES Users Workshop, Zagreb
Distance between millichannels vs. millichannel-sample distance.
Melting points : 176Yb2O3 , 2628K
Backing, Cu , 1358 K
Oulet Water
Inlet Water
Deuteron
Beam
Simulation for 1.25 mA
Temperature (Solid) [K]

## Slide 21: 2. Radioisotope Production at IFMIF-DONES Proposal of realistic targets and cooling system design for deuterons
M. Elena López Melero
Third DONES Users Workshop, Zagreb
Flow Simulation with SolidWorks tools.
Temperature distributions:
176Yb2O3 :
Φ =20 mm, t=0.25 mm
3.5 l/min Fluid Flow Rate
Temperatures below melting points !

## Slide 22: 2. Radioisotope Production at IFMIF-DONES Proposal of realistic targets and cooling system design for deuterons
M. Elena López Melero
Third DONES Users Workshop, Zagreb
Structural Simulation with SolidWorks tools.
Stress studies:
Pre-sample cut plot
Post-sample cut plot

## Slide 23: X. 177Lu Yield with deuterons
M. Elena López Melero
Third DONES Users Workshop, Zagreb
600 µm sample thickness
Energy range: [11.0-22.6] MeV
Reaction | Location | Irradiation Time (days) | Activity (GBq) | Specific Activity (GBq/mg)
176Yb(n,)177Yb177Lu | Nuclear Reactor | 7 | 590 | 1.11
176Yb(d,)177Lu | 0.1% initial beam |  | 200 | 0.13
Reaction | Location | Irradiation Time (days) | Activity (GBq) | Specific Activity (GBq/mg)
 | Nuclear Reactor | 7 | 590 | 1.11
 | 0.1% initial beam |  | 200 | 0.13