## Slide 1
J. Mollá, M. Sánchez-Arenillas, S. Hendricks, B. Garcinuño, J. Patiño. (Fusion National Laboratory, CIEMAT)
Design of LITEC experimental equipment 2023

## Slide 2: Introduction
LITEC
Li Loop not including any experimental device (neither traps nor monitors)
1:1 scale of the IFMIF/DONES ICS
Execution of experiments for testing and validation of impurity monitors and impurity traps to be used in the Impurities Control System of DONES.
Getter material for the N trap
Cold Trap (O)
H-Trap
Resistivimeter (N)
Plugging meter (O)
Electrochemical meter (H)
LITEC equipment to be installed and commissioning later

## Slide 3: Introduction / LITEC equipment inst.,comm.& experiments
LITEC Commissioning (end of construction contract)
Resistivimeter commissioning
CT commissioning
NT getter commissioning
Plugging meter commissioning
Sampler test and commissioning of chemical analysis lab.
Electrochemical H monitor commissioning
Comparison with chemical anal.
NT getter and resistivimeter experiments
CT and plugging meter experiments
HT and electrochemical H monitor experiments
Impurities injection systems commissioning and experiments
Check out of basic systems (heating and temp. Control, pump and flowmeter, safety sys., sample extraction …
Extraction of samples and chemical analysis to check that we are able to do it
Check that we are able to measure something representative of the impurity content
Reduction of the O content down to acceptable level for N getters
Reduction of the N content down to acceptable level (corrosion)
Checkup that we are able to introduce different kind of impurities and measure to which extent we can control the process
Experimental program related to the NT (if required)
Experimental program related to the CT and the plugging meter
Experimental program related to the HT and the electrochemical H-monitor
Permeation-based H-monitor
Testing feasibility of this kind of monitor
LITEC Equipment Des. & Manuf.
LITEC Exp. Programme
LITEC Equipment commissioning

## Slide 4: Introduction
Activities 2022:
  Design of Experimental Programme to be executed in LITEC for validation of impurity Control in the Li loop (completed)
Activities 2023:
  Manufacturing of the H-trap for LITEC (on-going, almost completed)
  Basic technical requirements and specifications for the LITEC Cold-trap prototype (completed)
  Conceptual design for LITEC plugging meter (completed)
Activities 2024:
  Manufacturing of the Cold-trap for LITEC (on-going, starting)

## Slide 5: Experimental Programme to be executed in LITEC
Cold Trap and plugging monitor experiments
Hydrogen Trap and electrochemical H sensor experiments

## Slide 6: Experimental Programme to be executed in LITEC
Cold Trap and plugging monitor experiments
  Plugging monitor state of the art
  Cold trap state of the art
  Assumptions
  Cold Trap equations
  Experiments to be performed for testing the cold trap and the plugging monitor
  Expected outcomes from experiments to be performed for testing the cold trap and the plugging monitor
Hydrogen Trap and electrochemical H sensor experiments
  …

## Slide 7: Experimental Programme to be executed in LITEC
Cold Trap and plugging monitor experiments
  …
Hydrogen Trap and electrochemical H sensor experiments
  Electrochemical H sensor: state of the art
  H-trap state of the art
  Assumptions
  H-trap equations
  Typical experiment proposed for testing the H-trap and the monitoring system
  Experimental parameters (temperature, flow rate, Y amount and shape, …) to be studied
  Thermal desorption experiments (for potential recovery of Y getter material)
  Expected outcomes following the experimental campaign of the H-trap and the electrochemical H-sensor

## Slide 8: Introduction
Activities 2022:
  Design of Experimental Programme to be executed in LITEC for validation of impurity Control in the Li loop (completed)
Activities 2023:
  Manufacturing of the H-trap for LITEC (on-going, almost completed)
  Basic technical requirements and specifications for the LITEC Cold-trap prototype (completed)
  Conceptual design for LITEC plugging meter (completed)
Activities 2024:
  Manufacturing of the Cold-trap for LITEC (on-going, starting)

## Slide 9: Manufacturing of the H-trap for LITEC
Design performed by IDOM
Starting point: Technical requirements defined by Ciemat
ED by IDOM was the staring point for the manufacturing at Ciemat

## Slide 10: Manufacturing of the H-trap for LITEC
Work done and Present status:
3D model adapted to the Ciemat workshop manufacturing possibilities
Production of manufacturing drawings
Procurement of materials: On going; almost completed waiting for some piping
Manufacturing of components: On going; almost completed waiting for some piping
Welding and assembly: On going; almost completed waiting for some piping


Missing pipes

## Slide 11: Manufacturing of the H-trap for LITEC
Cylindrical body
Conical transition
Vessel cover
Vessel bottom
Outlet pipe

## Slide 12: Manufacturing of the H-trap for LITEC
Inner getter container
Upper flange
Supporting structure
Fixing elements

## Slide 13: Manufacturing of the H-trap for LITEC
Manufacturing conical transition

## Slide 14: Introduction
Activities 2022:
  Design of Experimental Programme to be executed in LITEC for validation of impurity Control in the Li loop (completed)
Activities 2023:
  Manufacturing of the H-trap for LITEC (on-going, almost completed)
  Basic technical requirements and specifications for the LITEC Cold-trap prototype (completed)
  Conceptual design for LITEC plugging meter (completed)
Activities 2024:
  Manufacturing of the Cold-trap for LITEC (on-going, starting)

## Slide 15: Basic technical requirements and specifications for the LITEC Cold-trap prototype
Summary
  Li volume: 100 l
  Crystallization surface: 55 m2
  Maximum size: 2.5 m height, 1.5 m in horizontal directions
  Operation temperature: 190ºC - 350ºC
  Maximum temperature at external insulating layer: 50ºC
  Maximum pressure: 6 bar
  Pressure drop: 0.6 bar
  Maximum weight: 600 kg
  Flow rate. 0,4 l/s – 2 l/s
Available in IDM: https://idm.euro-fusion.org/?uid=2QPCKJ

## Slide 16: Introduction
Activities 2022:
  Design of Experimental Programme to be executed in LITEC for validation of impurity Control in the Li loop (completed)
Activities 2023:
  Manufacturing of the H-trap for LITEC (on-going, almost completed)
  Basic technical requirements and specifications for the LITEC Cold-trap prototype (completed)
  Conceptual design for LITEC plugging meter (completed)
Activities 2024:
  Manufacturing of the Cold-trap for LITEC (on-going, starting)

## Slide 17: Conceptual design for LITEC plugging meter
Plugging monitor
Chem. Analysis
Temperature decrease produce a drop of flow rate
Saturation temperature  dQ/dt=0 (max. and min)
O content is derived accurately from the temperature dependence of solubility
Measurement of flow rate decrease due to precipitates in a thin channel determines the precipitation temperature  Determination of O content

## Slide 18: Conceptual design for LITEC plugging meter
Bibliography revision  State of the art
  Several procedures and geometries tested since the 60’s in Na loops
Proposed procedure:
  Oscillating plugging meter: the control system adjust the temperature to keep the flow rate close to a predefined set value
  The temperature of the plugging meter is used also to set the cold trap temperature

## Slide 19: Conceptual design for LITEC plugging meter
Proposed conceptual design based on the latest reference found (Mangus, 2021)
Document available in the : https://idm.euro-fusion.org/?uid=2RJ7S9
Plugging orifice plate (several geometries may be tested)

## Slide 20: Introduction
Activities 2022:
  Design of Experimental Programme to be executed in LITEC for validation of impurity Control in the Li loop (completed)
Activities 2023:
  Manufacturing of the H-trap for LITEC (on-going, almost completed)
  Basic technical requirements and specifications for the LITEC Cold-trap prototype (completed)
  Conceptual design for LITEC plugging meter (completed)
Activities 2024:
  Manufacturing of the Cold-trap for LITEC (on-going, starting)

## Slide 21: Manufacturing of the Cold Trap
Cylindrical body: DN500 pipe
Vessel bottom cap: cap for DN500 pipe
Flange: non-standard flange
Upper counter flange
Mechanical support
Metallic mesh, 125 discs
With the exception of the flange and counter-flange, the main components may be purchased in standard industry

## Slide 22: Conclusions
Activities 2022:
  Design of Experimental Programme to be executed in LITEC for validation of impurity Control in the Li loop (completed)
Activities 2023:
  Manufacturing of the H-trap for LITEC (on-going, almost completed)
  Basic technical requirements and specifications for the LITEC Cold-trap prototype (completed)
  Conceptual design for LITEC plugging meter (completed)
Activities 2024:
  Manufacturing of the Cold-trap for LITEC (on-going, starting)