## Slide 1
Assessment of radioisotopes production in IFMIF-DONES Test Cell
F.Mota*, M.I. Ortiz, E. López-Melero, I. Porras, J. Praena, M. Alcantud, N. Ballesteros, A. Dilla, E. Fernández, J.Gallo, J.C. Marugan, C. Prieto, I. Cobo, O. Oliva, D. Terán

## Slide 2
Index
Why use IFMIF-DONES for Radioisotope production
Assessment of the 99Mo production in IFMIF-DONES
High level requirements of the RadioIsotope Production Device (RIPD)
Proposals of concepts design for the RIPD
99Mo assessment production considering the first RIPD mockups
Radioisotope production device vs Neutron Spectral Shifter
Conclusions and Future works

## Slide 3
Index
Why use IFMIF-DONES for Radioisotope production
Assessment of the 99Mo production in IFMIF-DONES
High level requirements of the RadioIsotope Production Device (RIPD)
Proposals of concepts design for the RIPD
99Mo assessment production considering the first RIPD mockups
Radioisotope production device vs Neutron Spectral Shifter
Conclusions and Future works

## Slide 4
99Mo is the precursor of Technetium-99m (99mTc), which is used for radiopharmaceutical applications
99mTc are used in Single Photon Emission Computed Tomography (SPECT) Thanks to its short half-life T1/2 (6 h) and the 140 keV γ-ray emission
Ideal features for imaging and low radiation dose to the patient
Radiopharmaceuticals based on 99mTc are used in more than 30 million procedures per year, accounting for about 85% of all nuclear medicine diagnostics
However, a global shortage of 99Mo emerged in the late 2000s because of the frequent shut down due to extended maintenance periods of the main reactors for 99Mo production: NRU Chalk River Reactor (Canada) and the High Flux Reactor (HFR) at Petten (The Netherlands).
99Mo is currently produced in nuclear fission reactors as a by-product of 235U fission.
Why use IFMIF-DONES for Radioisotope production

## Slide 5
However the 100Mo(n,2n)99Mo cross section has a threshold energy at about 7 MeV then this way of production is not reached by conventional reactors.
Neutron Energy of Fission below 7 MeV
An alternative of 235U fission method is to irradiate directly Molybdenum to produce 99Mo. It is produced by two ways the 98Mo(n,γ)99Mo and 100Mo(n,2n)99Mo reactions.
DONES neutron source up to 55 MeV
98Mo(n, γ)99Mo
100Mo(n, 2n)99Mo
1.17 %
98.83 %
Ratio
Taking into account that only there is a 9.82 % of 100Mo in a natural composition, higher amount of 99Mo could be obtained enriching the Molybdenum in 100M.
98Mo(n, γ)99Mo
100Mo(n, 2n)99Mo
1.17 %
98.83 %
Ratio
Taking into account that only there is a 9.82 % of 100Mo in a natural composition, higher amount of 99Mo could be obtained enriching the Molybdenum in 100M.
Why use IFMIF-DONES for Radioisotope production

## Slide 6
Index
Why use IFMIF-DONES for Radioisotope production
Assessment of the 99Mo production in IFMIF-DONES
High level requirements of the RadioIsotope Production Device (RIPD)
Proposals of concepts design for the RIPD
99Mo assessment production considering the first RIPD mockups
Radioisotope production device vs Neutron Spectral Shifter
Conclusions and Future works

## Slide 7
Irradiation time determination of the molybdenum samples of MoO3
After 6 days of irradiation the sample is extracted from the TC to be purified and then transported outer the IFMIF-DONES installation
After 6 days of irradiation the sample is extracted from the TC to be purified and then transported outer the IFMIF-DONES installation
Assessment of the 99Mo production in IFMIF-DONES

## Slide 8
6 irradiation day | Activity (GBq/g Mo)
Behind of HFTM | 51
Just in front of Duct | 2.24
The 100Mo(n,2n) and 98Mo(n,γ) reaction have been taken into account for the 99Mo production
“The (n, γ) process produces 99Mo of relatively low specific activity, from a low of 3.7 GBq/g to a high of 74 GBq/g depending on the neutron flux available in the reactor”.
6 irradiation day | Specific Activity (GBq/g Mo)
Behind of HFTM | 51
Just in front of Duct | 2.24
The 100Mo(n,2n) and 98Mo(n,γ) reaction have been taken into account for the 99Mo production
“The (n, γ) process produces 99Mo of relatively low specific activity, from a low of 3.7 GBq/g to a high of 74 GBq/g depending on the neutron flux available in the reactor”.
Assessment for 99Mo production in the TC area
Assessment of the 99Mo production in IFMIF-DONES

## Slide 9
~8 cm
20 cm
Considering an average production of 44 GBq/g in the Mesh and taking into account a density of 3.17 g/cm3 of Mo in 4.69 g/cm3 of 100MoO3 and mesh volume of 100 cm3, the total activity reached of 99Mo would be about 14 TBq after 6 days of irradiation.
It would supply 99Mo generators to cover the demand of Andalucía (100 GBq per 99mTc generator)
Sensitivity analysis of the 99Mo production behind of HFTM
Mesh used for Neutron spectra calculation
Assessment of the 99Mo production in IFMIF-DONES

## Slide 10
High level requirements of the RadioIsotope Production Device (RIPD)
Do not disturb the normal operation of the IFMIF-DONES.
The targets should be introduced and extracted in periods of 6-day without opening the TC
Automatic insertion and extraction of targets
mechanical or pneumatic extraction and insertion
Lateral or vertical access
To keep the integrity of the TC shielding
The target has to be solid or encapsulated to avoid contamination
Maximization of the irradiation volume to maximize the production rate.
The handling of the targets has to be done remotely.
The system must be cooled to maintain a constant temperature during irradiation.
Having an Hot Cell for handling irradiated targets.
To define specific safety protocols to insertion, extraction, purification and introduction in generators to be exported to Hospitals and research centers.

## Slide 11
Index
Why use IFMIF-DONES for Radioisotope production
Assessment of the 99Mo production in IFMIF-DONES
High level requirements of the RadioIsotope Production Device (RIPD)
Proposals of concepts design for the RIPD
99Mo assessment production considering the first RIPD mockups
Radioisotope production device vs Neutron Spectral Shifter
Conclusions and Future works

## Slide 12
Transverse duct for sample
Shielding plug during samples extraction
Shielding plug during irradiation
Proposals of EAI (to meet with the high level requirements)
Proposals of concepts design for the RIPD
100Mo sample holder
Ø =20 cm
The dimensions of each plate is 0.9x27.5x11.4 cm3. (V=282.15 cm3)
The dimensions of each plate is 0.9x27.5x11.4 cm3. (V=282.15 cm3)
Ø =28.5 cm
The sealing of the inner of the TC is kept
R158
Based on the Japanese proposal (O. Nasayiuki, FED 2021))
PROPOSAL 1: lateral mechanical sample insertion device for Radioisotope production

## Slide 13
Proposals of concepts design for the RIPD
PROPOSAL 2: lateral sample insertion using a Rabbit system
Transference table
Transverse duct for sample
Spherical specimens of 10.5 mm diameter
Inside the duct there are several smaller ducts to transport the spherical specimens. Inner diameter of the duct could be 13 mm

## Slide 14
Index
Why use IFMIF-DONES for Radioisotope production
Assessment of the 99Mo production in IFMIF-DONES
High level requirements of the RadioIsotope Production Device (RIPD)
Proposals of concepts design for the RIPD
99Mo assessment production considering the first RIPD mockups
Radioisotope production device vs Neutron Spectral Shifter
Conclusions and Future works

## Slide 15
D+
D+
Shielding
The dimensions of each plate is 0.9x27.5x11.4 cm3. (V=282.15 cm3)
The length from HFTM to the Radioisotope Production Device is 1.3 cm
The length from HFTM to the first 100MO3 plate is 8 cm
The distance between 100MoO3 plates is 1.1 cm
Neutron transport calculations performed to determine the 99Mo production rate considering proposal 1
99Mo assessment production considering the first RIPD mockups

## Slide 16
Enriched MoO3 (95% 100Mo) | SPECIFIC ACTIVITY GBq/g 100Mo | ACTIVITY (TBq)
Plate 1 | 24.14 | 21.59
Plate 2 | 20.85 | 18.65
Plate 3 | 17.81 | 15.93
Plate 4 | 15.24 | 13.63
TOTAL |  | 69.80
99Mo activity obtained in each plate after 6 days of irradiation using an average neutron fluence rate in each plate.
1 2 3 4
Considering that one 99mTc generation has about an activity of 46 GBq, which could be equivalent to considering a 100 GBq just before taking out the sample.
99Mo assessment production considering the first RIPD mockups
Under these conditions, it is possible to produce ~ 69.80 TBq de 99Mo/99mTc, per week
It means that we could obtain about 700 generators per week
Taking into account that a hospital could need 2 generators per week, we could supply to 350 hospitals.

## Slide 17
Index
Why use IFMIF-DONES for Radioisotope production
Assessment of the 99Mo production in IFMIF-DONES
High level requirements of the RadioIsotope Production Device (RIPD)
Proposals of concepts design for the RIPD
99Mo assessment production considering the first RIPD mockups
Radioisotope production device vs Neutron Spectral Shifter
Conclusions and Future works

## Slide 18
The Radioisotope production device could have a similar effect like the Neutron Spectral shifter module (NSS) due to the 100Mo(n,2n)99Mo reaction
Radioisotope production device vs Neutron Spectral Shifter
D+

## Slide 19
Index
Why use IFMIF-DONES for Radioisotope production
Assessment of the 99Mo production in IFMIF-DONES
High level requirements of the RadioIsotope Production Device (RIPD)
Proposals of concepts design for the RIPD
99Mo assessment production considering the first RIPD mockups
Radioisotope production device vs Neutron Spectral Shifter
Conclusions and Future works

## Slide 20
Conclusions and Future works
A 99Mo production assessment has been performed in IFMIF-DONES TC taking in advance the neutrons that cross the HFTM.
Two mock-ups for the Radioisotope production devices have been proposed.
Considering the mechanical insertion proposal conditions, it would be possible to cover the necessities of 350 hospitals of ~99Mo/99mTc per week.
The works are ongoing to validate the different RIPD concepts proposed respect to the productions rates, radiation hazards, safety issues and design analysis.
Then, the benefit of radioisotope production in IFMIF-DONES has been demonstrated starting from the assessment production of one of the most demanding radioisotopes for cancer diagnostics. This could mean a great social benefit since the demand of a large number of inhabitants could be covered and a great benefit for IFMIF-DONES project, on the one hand for its social impact and on the other because it could mean important funding for IFMIF-DONES operation.