## Slide 1: Impact of installation of the Tritium Release Test Module in the IFMIF-DONES Test Cell on the neutron spectra inside the Complementary Experiments Room collimated by Neutron Beam Tube and Shutter
A. Serikov 1, G. Zhou 1, Y. Qiu 1, B. Bienkowska 2, R. Prokopowicz 3
1 Karlsruhe Institute of Technology (KIT), Institute for Neutron Physics and Reactor Technology, Eggenstein-Leopoldshafen, Germany
2 Institute of Plasma Physics and Laser Microfusion, Warsaw, Poland
3 National Centre for Nuclear Research (NCBJ), Otwock-Swierk, Poland

## Slide 2
Neutronics analyses for DONES Test Cell and CER
To conduct variety neutronics experiments, collimated neutrons from the DONES Test Cell (TC) will be directed to Complementary Experiments Room (CER) through the Neutron Beam Tube and Shutter (NBT&S) system.
Neutronics analyses performed in this work continue the task of neutron spectra assessments [1] inside the Complementary Experiments Room (CER) collimated by the Neutron Beam Tube and Shutter (NBT&S) system. The NBT&S system is developed to supply neutrons from the D-Li target of the IFMIF-DONES Test Cell (TC) to the CER (Room R160) for conducting experiments with neutron spectra variated from fast to thermal.
The neutron and photon radiation transport has been performed by the McDeLicious-17 code package – MCNP modification, which simulates the deuteron-lithium (d-Li) nuclear reactions.The neutronics results were normalized to a 125 mA deuteron beam of 40 MeV deuterons impinging the lithium target.
As fusion neutrons are necessary for Breeding Blanket qualification, it is proposed in this work to place the irradiated breeding materials close to the D-Li neutron source, where the materials get the highest neutron loads and, therefore, the space is most valuable for materials irradiation. Such space is behind the High Flux Test Module (HFTM), in the region of the Medium Flux Test Module (MFTM). In this work, initial steps in developing the neutronics models to simulate the radiation conditions suitable for the breeding two .
  Tritium Release Test Module (TRTM) - geometry has been implemented into the final reference test cell model at the EVEDA phase [2], with updates during the DONES PreP phase.
  DEMO Helium Cooled Pebble Bed (HCPB) Breeding Blanket (BB) module – as module is large, DONES D-Li source could not cover uniformly the whole FW surface of the BB. Therefore, decision was to perform neutronics analyses to test the HCPB BB in radiation conditions of DONES MFTM, and based on the results of the performed analyses, decide about the conceptual designing as a potential “Other” Irradiation Module (OIM) in DONES.
Reference:
[1] A. Serikov et al., “Neutrons supply to the IFMIF-DONES Complementary Experiments Room through the neutron tube and neutron beam shutter”, First IFMIF-DONES Users Workshop, September 26-27, 2022, https://agenda.ciemat.es/event/3879/contributions/4128/.
[2] K. Kondo et al., “Neutronic Analysis of the IFMIF Tritium Release Test Module Based on the EVEDA Design”, Fusion Science and Technology, 66:1 (2014), 228-234, https://doi.org/10.13182/FST13-74310.13182/FST13-743

## Slide 3: Introduction
We propose to develop OIM based on the actual version of the HCPB BB because its implementation permits a wide scope of neutron irradiation and material tests. Nuclear, thermal hydraulic and thermal-mechanical analyses confirmed soundness of the HCPB BB design [3].
Ref.[3] G. Zhou, et al., “Solid Breeding Blankets: overview and key pending validation needs,” Second IFMIF-DONES Users Workshop, Granada, October 2023.
HCPB Breeding Blanket (BB) module

## Slide 4: Developed MCNP models for two breeding concepts: TRTM and HCPB BB inside DONES TC Horizontal cross-sections of the two MCNP models
TRTM
HCPB BB
NSS
HFTM
TRTM
TRTM graphite reflectors:
back-side
lateral
NSS
HFTM
7 full-size pins of HCPB BB integrated inside DONES TC:
EU DEMO HCPB BB design:
Advanced ceramic breeder ACB pebbles (lithium orthosilicate, 35mol% lithium metatitanate)
Titanium beryllide
Structural steel: Eurofer97
1)-blue, 2) –green, 3)- magenta

## Slide 5: Developed MCNP models for two breeding concepts: TRTM and HCPB BB inside DONES TC Vertical cross-sections of the two MCNP models
TRTM
HCPB BB

## Slide 6
7 full-size pins of HCPB BB integrated inside DONES TC
EU DEMO HCPB BB design:
Advanced ceramic breeder ACB pebbles (lithium orthosilicate, 35mol% lithium metatitanate), Li4SiO4 +35% Li2TiO3, Li6 = 60% dens = 1.753 g/cc;
Titanium beryllide;
Structural steel: Eurofer97.
1)-blue, 2) –green, 3)- magenta

## Slide 7
Nuclear heat map overlayed with the BB pin geometry modeled with MCNP.
The overlayed map represents the nuclear heat in Be12Ti calculated at the first wall of the HCPB BB model with 7 full-size breeder pins.

## Slide 8
Y=3.7 cm
Heating data along the axial line at a distance of Y=3.7 from the central x-axis.
That is the distance of Li-ceramic pebbles.
X
0

## Slide 9
1
2
3
4
Four axial profiles of volumetric nuclear heating (W/cc) in separate materials

## Slide 10
Profile #1 of volumetric nuclear heating (W/cc) in Li-ceramics at a distance of Y=3.7 cm

## Slide 11
Profile #2 of volumetric nuclear heating (W/cc) in EUROFER at a distance of Y=4.5 cm

## Slide 12
Profile #3 of volumetric nuclear heating (W/cc) in Be12Ti-inner block at a distance of Y=1 cm

## Slide 13
Profile #4 of volumetric nuclear heating (W/cc) in Be12Ti-outer block at a distance of Y=7 cm

## Slide 14
Four iso-surfaces of total n-flux:
5e13
1e13
5e12
1e12

## Slide 15
View on the Total Neutron Flux to show similarity with the Six-Petal Narcissus Flower

## Slide 16
Central slice by plane PZ=0 perpendicular to the Z-axis

## Slide 17
5e13
1e13
5e12
1e12
1e12

## Slide 18: T-production rate in ACB pebbles map with 1D plot along the axial line at a distance of Y=3.7 from the central x-axis. Case of one accelerator beam run I=125 mA
1-Accelerator run: Max T-production in ACB ~1.7e18 / 1.75/1e6 = 9.71e+11 atoms-T/g-ACB/s ~1e12 atoms-T/g-ACB/s

## Slide 19: T-production rate in ACB pebbles map with 1D plot along the axial line at a distance of Y=3.7 from the central x-axis. Case of two accelerators’ beam run I=250 mA
2-Accelerators run: Max T-production in ACB ~3.4e18 / 1.75/1e6 = 1.94e+12 atoms-T/g-ACB/s ~ 2e12 atoms-T/g-ACB/s

## Slide 20
TC liner = 25 mm
Actual CAD model of the TC liner:
TC liner = 35 mm
100 mm TC bottom plate
TC liner = 25 mm
TC liner thickness shift from 35 mm to 25 mm
Grooved TC liner = 8 mm
25 mm
35 mm
Border line
35-25-8 mm composed TC liner

## Slide 21: CAD model of the actual design of RBSB
RBSB design characterized:
5-cm liners (SS316L steel)
4-cm gaps
The gaps are shifted in a dog-leg shape to prevent neutron and gamma streaming.
The shielding filling of the RBSB is composed of Heavy concrete with rebar and water/pipe mixture. The shielding filling has density 3.495 g/cc.
shielding filling
5-cm liners
CAD view of 5-cm liners
Horizontal cut of the RBSB design

## Slide 22: MCNP material numbers set at horizontal cut pz=0:
TC neutronics model update 2022: design of RBSB with liners
Bucket
M13 = SS316L, density 7.93 g/cc - Steel
M22= Ordinary Concrete, 2.33 g/cc - Bucket
M33 = Lithium with impurities, density 0.512 g/cc
M45 = “Microtherm” thermal insulation, 0.35 g/cc
M105 = Lithium pipe heater mixed with SS316L shielding, 6.3867 g/cc
M201 = Heavy concrete with rebar, 3.513 g/cc
M202 = Heavy concrete with rebar and water/pipe mixture,
density 3.495 g/cc- RBSB filling
M203 = TC liner cooling layer, 1.1438 g/cc, its mixture composed of materials with the following volume fractions: Water(M43): 20.345% , SS316L pipe (M13): 10.30%, kaowool (M23): 68.885%, Aluminum(M34): 0.5%.
RBSB

## Slide 23: Neutron flux computations in TC-CER using the MCNP mesh-tallies
Maps of neutrons streaming from Test Cell (TC) through the Neutron Beam Tube and Shutter (NBT & S) system to CER. The collimated neutrons will be supplied to conduct variety neutronics experiments inside CER.
NBTube
Area covered by MCNP mesh-tally
Column
Test Cell (TC)
Compl. Exp. Room (CER)
R160

## Slide 24: Collimated neutrons in CER : Neutron Beam Tube and Shutter (NBT & S) system
Subject: Analyses of neutron fluxes in broad energy groups at the entrance to CER from TC through the open NB shutter.
Method: Using OTF variance reduction, n-fluxes maps have been calculated with MCNP mesh-tallies of in three e-groups :
Thermal neutron flux (En< 0.625E-6 MeV)
Epithermal neutron flux (0.625E-6 MeV<En< 0.5 MeV)
Fast neutron flux (0.5 MeV<En<100 MeV)
In all the presented MCNP calculation results, all channels of the NB shutter have been empty.
The position of “open NB shutter” is formed when the NB shutter central channel coincides with the NB Tube.
The “closed NB shutter” – when all channels inside the rotated “Revolver-type” drums are at the farthest position to the NB Tube.
In future studies, the 5 open channels in the last drum will be filled with materials to function as neutron filters and neutron spectral shifters.
Central open channel
NB shutter

## Slide 25: Neutron dose rate maps for two positions of the NB shutter
1e5
1e3
0.5
3
10
Position #1: Open NB shutter
Position #2: Closed NB shutter
CER is Yellow (limited regulated) rad. zone: (10<DR<1e3) microSv/h
CER is Red (forbidden) radiation zone: DR>1e5 microSv/h
1e5
1e3
0.5
3
10
1e5
1e5

## Slide 26
Neutron maps in TC & CER
for the MCNP model with empty DONES TC behind HFTM

## Slide 27
High resolution (2-cm) mesh-tally around NB-shutter

## Slide 28: High resolution (2-cm) mesh-tally around NB-shutter

## Slide 29: High resolution (2-cm) mesh-tally around NB-shutter

## Slide 30
1e9
1e8
1e7
1e6
1e10
1e11
Total n-flux with open NB shutter and 8 mm TC liner
1e11
1e10
TC wall
CER

## Slide 31
1e9
1e8
1e7
1e6
1e10
1e11
Fast (En>0.5 MeV) n-flux with open NB shutter and 8 mm TC liner
1e11
1e10
TC wall
CER

## Slide 32
1e9
1e8
1e7
1e6
1e10
1e11
Epithermal neutron flux (0.625E-6 MeV<En< 0.5 MeV), open NB shutter, 8 mm TC liner
1e11
1e9
TC wall
CER

## Slide 33
Neutron maps in TC & CER
for the MCNP model with HCPB BB in DONES TC behind HFTM

## Slide 34
HCPB BB module - Total neutron flux horizontal central cut at entrance to CER from TC

## Slide 35
HCPB BB module - Total neutron flux horizontal central cut at entrance to CER from TC

## Slide 36
HCPB BB module - Fast neutron flux

## Slide 37
HCPB BB module - Thermal neutron flux

## Slide 38
Neutron maps in TC & CER
for the MCNP model with TRTM in DONES TC behind HFTM

## Slide 39
TRTM total neutron flux horizontal central cut at entrance to CER from TC
CER
TC
RBSB + TC Bucket concrete

## Slide 40
TRTM fast neutron flux
CER
TC
RBSB + TC Bucket concrete

## Slide 41
TRTM total & fast neutron fluxes – Overlaid maps
CER
TC
RBSB + TC Bucket concrete
Total contour
Fast contour

## Slide 42
TRTM thermal neutron flux
CER
TC
RBSB + TC Bucket concrete
Detector #1 – sphere R=20cm
Detector #2 - sphere R=20cm

## Slide 43: Six detectors in open NB-shutter configuration (two spheres and four disks)
Detector #1 – sphere R=20cm
Detector #2 - sphere R=20cm
Detector #3
Detectors #4, 5, 6
at open channels
Neutron Beam (NB) shutter with open channels
CAD model
MCNP model

## Slide 44: Disk detectors at the entrance to CER (R160)
Detectors #4, 5, 6 outside the five open channels of revolving drum
Detector #3
Det. #3 is a truncated disk with thickness d=5 cm, radius R=200 cm
The 5 open holes of Detectors #4, 5, 6 coincide with 5 open channels of rotated “Revolver-type” drum. The dominate radiation streaming was detected in the central open channel.
Central open channel

## Slide 45: Disk detectors at the entrance to CER (R160)
c ccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccc
c detector behind the NB shutter:
90004 301 -1.2E-3 -90004 11529 50138
(50127 50128 50129 50130 50131)
imp:n=1 imp:p=1 $ tally for NB shutter
c detector for open channels in NB shutter:
90005 301 -1.2E-3 -90004 11529 50138
(-50127:-50128:-50131)
imp:n=1 imp:p=1 $ tally for open channels in NB shutter
c detector for open channels in NB shutter:
90006 301 -1.2E-3 -90004 11529 50138
-50129
imp:n=1 imp:p=1 $Central open channel of the NB shutter
90007 301 -1.2E-3 -90004 11529 50138
-50130
imp:n=1 imp:p=1 $ Side open channel of the NB shutter
c ccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccc
Detector #3: MCNP cell #90004 - air of truncated disk with thickness d=5 cm and radius R=200 cm – Outside all 5 disks
Detector #5: MCNP cell #90006 - air of central open channel
Detector #4: MCNP cell #90005 - air of three side detectors, far from open
Detector #6: MCNP cell #90007 - air of one side channel, neighboring to open
Detector #6
Detector #5
Detector #4
Detector #3
Detector #7 = United disk detector for all disk detectors (3+4+5+6)

## Slide 46: Volumes of disk detectors at the entrance to CER (R160)
Detector #6
Detector #5
Detector #4

## Slide 47
Chart: Total neutron flux at 7 CER detectors for 5 variants of TC configurations
TC liner 8 mm | 875210936993.431 | 608573687239.6069 | 32321350.0329 | 108910243.2363 | 21516078240.0666 | 268980041.6976 | 65094597.2336
TC liner 15 mm | 858753321159.3347 | 566097222365.1687 | 27206199.1736 | 91769368.9326 | 18227744524.418 | 225148633.558 | 54965870.6271
TC liner 25 mm | 814665412486.0911 | 567822064060.9271 | 21468533.1601 | 72078714.1224 | 14739430218.7264 | 179597995.9746 | 43906336.6273
TRTM inside TC (8 mm liner in front of NBT) | 236403579933.0511 | 945096867223.4767 | 470005.6678 | 1465514.5714 | 216685508.6434 | 4372487.8513 | 803118.0435
HCPB BB inside TC (8 mm liner in front of NBT) | 207539935756.7809 | 920337331670.3494 | 171775.1703 | 592176.5553 | 73379462.5319 | 1728965.7821 | 285289.0446

## Slide 49
Chart: Epithermal neutron flux (0.625E-6 MeV<En< 0.5 MeV) at 7 CER detectors for 5 variants of TC configurations
 | 561707530091.0154 | 440133047936.6937 | 11222239.7638 | 41368819.3708 | 1772550148.8609 | 100152492.8059 | 14119849.1238
 | 556998533212.2839 | 413078697047.8601 | 9382154.248 | 34622129.2143 | 1462406969.9484 | 83949370.1075 | 11776023.7003
 | 533107386817.4017 | 414478265828.6745 | 7374097.2606 | 26685616.0104 | 1112085466.0057 | 66017069.2385 | 9197585.4108
 | 187312436680.0348 | 726853662071.9264 | 223281.489 | 652047.7714 | 96865612.275 | 1974408.7008 | 372110.993
 | 166056597727.2361 | 706501723724.0503 | 85148.8739 | 302612.3324 | 48763741.0379 | 850910.1447 | 159947.1586

## Slide 50
Chart: Thermal neutron flux (En< 0.625E-6 MeV) at 7 CER detectors for 5 variants of TC configurations
 | 100867130924.1534 | 86089892873.5892 | 9662168.3579 | 33000374.914 | 705984021.0728 | 91833121.4066 | 10929050.7257
 | 101170321090.7435 | 83874456065.75 | 8069474.602 | 27400433.9153 | 587786437.898 | 75686561.1333 | 9122580.0598
 | 98468168572.5614 | 84138852214.9615 | 6438693.4115 | 22374240.107 | 469581029.8818 | 60546275.4669 | 7282361.9931
 | 36039940560.2837 | 123997616162.8958 | 190141.2171 | 618751.2076 | 19304442.704 | 1950352.9026 | 223228.5423
 | 31919717499.1528 | 120542262876.5313 | 76762.7439 | 263885.3286 | 8006020.0354 | 825129.5279 | 90557.1948

## Slide 51: Conclusions
The MCNP mesh-tally reveled the dominancy of fast neutrons in the total neutron flux at the exit from NB shutter to CER in the initial model without any MFTM. By adding breeding modules the spectrum is getting softer, allowing to conduct experiments in CER (R160) requesting more thermal neutrons. For this reason HCPB BB module is preferential.
References:
[1] R. Knitter, M.H.H. Kolb, U. Kaufmann, A.A. Goraieb, Fabrication of modified lithium orthosilicate pebbles by addition of titania, J. Nucl. Mater. 442 (2013) 433–436, https://doi.org/10.1016/j.jnucmat.2012.10.034.
[2] Christopher K. Dorn, et al., A review of physical and mechanical properties of titanium beryllides with specific modern application of TiBe12,
Fusion Engineering and Design, 84 (2009) 319-322, https://doi.org/10.1016/j.fusengdes.2008.11.009
Two MCNP neutronics models have been developed to simulate the radiation conditions in DONES MFTM suitable for the breeding:
  Tritium Release Test Module (TRTM)
  DEMO Helium Cooled Pebble Bed (HCPB) Breeding Blanket (BB) module – 7 full-size pins of Advanced ceramic breeder ACB pebbles (lithium orthosilicate, 35mol% lithium metatitanate), Li4SiO4 +35% Li2TiO3, Li6 = 60% - Ref. [1]. Titanium beryllide with the composition TiBe12 has been used for neutron multiplication. TiBe12 stands out from other beryllides for fusion because it has the highest neutron-multiplication characteristic, with the added benefit of higher temperature performance capability compared to beryllium metal [2].
Neutron broad group | Percentage of the group in HCPB BB model | Percentage of the group in TRTM model
Fast | 23.0% | 49.1%
Epithermal | 66.1% | 42.2%
Thermal | 10.9% | 8.7%
Neutron broad group | Percentage of the group in model without any MFTM
Fast | 88.5%
Epithermal | 8.2%
Thermal | 3.3%
Spectrum is getting softer
One accelerator gives the peaking T-production rate of 1e12 atoms-T/g-ACB/s in ACB of HCPB BB, by adding the second accelerator, the value is doubled: 2e12 atoms-T/g-ACB/s in ACB of HCPB BB.