## Slide 1: IFMIF-DONES: Planned experimental areas and general capabilities
S. Becerril, J. Castellanos, C. Meléndez, A. Zsakai, T. Dezsi, R. Michalczyk, U. Wiacek, A. Kurowski, G. Wojtania, R. Prokopowicz, G. Galazka, R. López, C. Prieto, I. Podadera, F. Arbeiter, D. Bernardi, W. Krolas, A. Ibarra
2nd DONES Users Workshop (19 – 20 October 2023)

## Slide 2
Spaces for tests and experiments
  Ground floor
  First floor
Test Cell (R130)
  Envelope and service plugs
  Neutron flux regions
  Other Irradiation Modules
  Ancillaries
R160
  Facility for experiments with neutrons
  Space and ancillaries
  Potential experiments with neutrons
R026
  Space and ancillaries
  D+ beam extraction modes
  Potential experiments
Other capabilities and systems potentially involved
Final conclusión
References
Contents

## Slide 3
Spaces for tests and experiments – Ground floor
R026  Complementary experiments based on D+ beam
  Below Accelerator Vault (R110)

## Slide 4
Spaces for tests and experiments – First floor
R130 (Test Cell)  Highest flux neutron irradiation area
R160  Experiments based on neutron beam
  Downstream to the TC
Some ancillaries rooms available

## Slide 5
Test Cell – Envelope and service plugs
Envelope available for modules to be irradiated inside the Test Cell
  1.3 - 1.5 m behind the Li target (X)
  1.5 m (Y)
  5.8 m high (Z)
Dedicated Piping and Cabling Plugs (PCP) for cablind and fluid service to the modules to be irradiated in the Test Cell
D+ beam
PCP
PCP
PCP
PCP

## Slide 6
Test Cell – High-flux region
High-flux irradiation region
More than 300 cc submitted to 12 dpa/fpy
Around 200 cc submitted to 16.7 dpa/fpy
Compatible with top-level requirements

## Slide 7
  [MEDIUM FLUX REGION] Behind the HFTM  Around 3·1013 n/(cm2·s)
  [LOW FLUX REGION] TC Liner walls downstream from the HFTM  Around 1·1012 n/(cm2·s)
Test Cell – Medium and low-flux neutron regions
Courtesy of Y. Qiu

## Slide 8
Test Cell – HFTM and Other Irradiation Modules
A
B
C
E
D
High Flux Test Modules (HFTM; A) for:
  Reduced Activation Ferritic Martensitic Steels (250 – 550 °C)
  Copper alloys (100 – 350 °C)
  SiC or Tungsten alloys (1100 – 1200 °C)
Creep Fatigue Test Module (CFTM; B) for:
  Reduced Activation Ferritic Martensitic Steels (250 – 550 °C)
  Vanadium alloys (750 – 800 °C)
  SiC or Tungsten alloys (1100 – 1200 °C)
Model Blanket Module (MBM) for:
  Material compatibility in the Breeder Zone (HCPB)
  Tritium Permeation
  Structural behaviour of materials submitted to high pressure
Tritium Release Test Module (TRTM; C) for:
  Ceramic Breeder materials or Berylium (300 - 1000 °C)
Liquid Breeder Validation Module (LBVM; D) for:
  Liquid breeder materials
Test Module for superconductors irradiated at cryogenic temperature
Low Flux Test module (LFTM; E) for:
  Vaccuum vessel materials
Others…
[See diverse talks about Irradiation Modules today and tomorrow: F. Arbeiter, G. Zhou, A. Spagnuolo, A. Venturini, B. Garciñuno, F. Mota, A. Serikov]
[See M. Serrano talk]

## Slide 9
Test Cell – Ancillaries
Test Systems Ancillaries (TSA)
  GICS (Gas Inventory Control System)
    Provides the gas specimen (He, Ar) and pressure inside.
  GPS (Gas Purification Unit)
    Conditions the atmosphere temperature and purity.
  WCS (Water Cooling System)
    Provides cooling to TC Liner and external TC components.
  HCS-LP (Helium Cooling System – Low Pressure)
    Provides helium cooling (3.5 bar) to the HFTM.
  HCS-MP (Helium Cooling System – Mid Pressure)
    Provides helium cooling to Other Irradiation Modules (OIM; PBS4.5).
Rooms for TSA
  R151 (Tritium Room)
    Purification Units for GPS, HCS-MP y HCS-LP
  R149
    GICS, rest of GPS, WCS, HCS-MP and HCS-LP
  R145-1
    TS LICS (Local Instrumentation and Control)
First-order assessment on space reservation to accommodate needs from Test Modules is ongoing
R151
R145-1
R149

## Slide 10
R160
R160 floor
R130
Courtesy of D. Oravecz
Neutron Beam Shutter
Neutron Beam Tube
R160 is fed by the neutron field produced in the TC through the stripping reaction (D+, Li)
The Neutron Beam Tube (NBT) provides a free channel downstream for neutrons coming from TC
Neutron Beam Shutter (NBS)
  Open  Enables experiments (access forbidden to R160)
  Closed  Limited access allowed (yellow area) while TC in working conditions
Neutron flux density at the exit of the Neutron Beam Shutter (open)  About 2·1010 n/(cm2·s)
Neutron moderators needed to adjust neutron spectrum for experiments
Appropriate shieldings inside the R160 likely necessary
Neutron Beam Dump  Foreseen to avoid production of secondary neutrons and photons (20 m away from NBS exit)
R160 – Facility for experiments with neutrons
[See specific talk tomorrow about the Neutron Beamline and Shutter]

## Slide 11
R160 – Facility for experiments with neutrons

## Slide 12
R160 – Space and ancillaries
R160 (292 m2; 8 m high)
  Placed downstream to the Test Cell (R130)
Test Systems Ancillaries (TSA)
  GICS (Gas Inventory Control System)
    Provides the gas specimen (He, Ar) and pressure inside.
  GPS (Gas Purification Unit)
    Conditions the atmosphere temperature and purity.
  WCS (Water Cooling System)
    Provides cooling to TC Liner and external TC components.
  HCS-LP (Helium Cooling System – Low Pressure)
    Provides helium cooling (3.5 bar) to the HFTM.
  HCS-MP (Helium Cooling System – Mid Pressure)
    Provides helium cooling to Other Irradiation Modules.
Rooms for TSA and Complementary Experiments with neutrons
  R151 (Tritium Room)
    Purification Units for GPS, HCS-MP y HCS-LP
  R149
    GICS, rest of GPS, WCS, HCS-MP and HCS-LP
  R163: Ancillary Room for Complementary Experiments
R149
R151
R149
R151
R163

## Slide 13
Fundamental particle physics studies with cold and ultra-cold neutrons
Neutron scattering experiments with moderated neutron beams
Experiments with samples exposed to neutrons
  Analysis of neutron-rich isotopes production by neutron induced fission
  Maxwellian-averaged capture cross-section for some stellar nuclear reactions by activation techniques with neutrons
  Analysis of radioisotope production routes by nuclear decay induced reactions
  Characterization of materials by radiation analysis (for medicine, chemistry, biology, forensics,…)
  Imaging techniques with neutrons
  Fast neutron irradiation of components, devices or bio-samples
  Medical treatment of patients using neutrons.
R160 – Potential experiments with neutrons

## Slide 14
R026 – Space and ancillaries
Area: 2609 m2
Height: 7.5 m (dashed area) / 8.5 m
Huge area likely able to include many ancillaries and appropriate shieldings for the experiments to be held in there.

## Slide 15
Injector
LEBT
RFQ
MEBT
Superconducting cavities
HEBT
5
8.3
13.9
21.3
30.3
40 MeV
0.1
Courtesy of D. Sánchez
R026
R026 – D+ Beam extraction modes
R026
D+ parisitic beam extraction between QP3 and QP4 of the HEBT  Very interesting also for quality management of the beam [see I. Podadera’s talk tomorrow about the D+ beam extraction]
Single Bunch extraction
  Meander vacuum line
  Kicker + Electrostatic septum + Septum magnet to extract and bend the parasitic beam by 34° downwards
  2 additional dipoles to complete the whole 180° of the beam
  4 quadrupole (QP) doublets to keep the parasitic beam focused
  Simultaneous to the irradiation of the Li target
Courtesy of M. Vázquez

## Slide 16
Injector
LEBT
RFQ
MEBT
Superconducting cavities
HEBT
5
8.3
13.9
21.3
30.3
40 MeV
0.1
Courtesy of D. Sánchez
R026
R026 – D+ Beam extraction modes
Beam extraction between QP3 and QP4 of the HEBT
Slow extraction
  Meander vacumm line
  Selection of macropulses by means of a switching field from a permanent chopper in LEBT section
  Optional chopper in MEBT section for tails removal of the macropulse
  Non-simultaneous operation. The irradiation of the Li target needs to be interrupted

## Slide 17
Main beam  D+ ion beam 125 mA / 40 MeV (5 MW) @ 175 MHz (CW, 5.7 ns period)
Single bunch extraction
  Extraction of a fraction (0.1 - 1%) of the beam @ 40 MeV
  For 0.1% case
    125 µA (averaged current)
    40 MeV
    175 kHz
    5 kW (averaged power)
  Bunch length < 10 ns
Slow extraction (whole beam)
  Based on a switching dipole solution
  Fastest chopper field switch = 50 ms
R026 – D+ Beam extraction modes
Example of bunch timing conditions (Single bunch)
Bunch extracted
1.8 ns
T = 5.7 ns
T = 3.9 ns
Shortest time to restore normal operation = 100 ms
Chopper activation every 10 s for 1% usage

## Slide 18
Neutron time-of-flight facility (n_TOF)
R026 – Potential experiments
With deuterons
  Production of radionuclides with a high intense deuteron beam
  Deuteron induced reactions
  Half-life measurements of long-lived isotopes
With pulsed neutron beam (ToF-DONES facility) A neutron production target is necessary
  Neutron cross section measurements
  Gamma-spectroscopy of nuclei produced in fast-neutron-induced fission reaction
  Investigation of pygmy dipole resonances (PDRs) via (n, n’γ) reaction

## Slide 19
Depending on the further definition of the experiments to be held other systems might be involved
  Radioactive Waste Treatment Systems (RWTS) for management of activated products produced during the operation of the experiments
  Heating, Ventilation and Air Conditioning (HVAC) for management of potential air contamination occured during the operation of the experiments in R026/R160.
  Other systems involved in the safety of the operation of the experiments.
  [See talk by C. Torregrosa’s about the safety implications of experiments in R026/R160]
  Other service systems like Service Gas System (SGS) and similar.
  Start-Up Monitoring Module (STUMM) for radiation field characterisation prior to irradiation of other modules in the Test Cell.
Facilities for Post-Irradiation Experiments (PIE) of the irradiated samples are under evaluation.
Further capabilities by extension to IFMIF (two accelerators)  All the systems are currently required to be designed such a way to enable its feasibility for an eventual extension to 2 accelerators.
Other capabilities and systems potentially involved

## Slide 20
IFMIF-DONES offers very high versatility and unique/very competitive range of capabilities for fusion-related critical needs and for experiments in other research areas both with neutrons (R160/R026) and deuterons (R026) of great interest for the community in many fields like: medical applications, fundamental physics, nuclear physics, micro-imaging techniques, radionuclide production and other industrial applications
Final conclusion

## Slide 21
References
L. W. Iskra et al., “Report on posible complementary experiments to be developed in DONES using deuterons”, DONES-PreP WP8.2-1
A. Pisent et al., “Evaluation of the extraction of a deuteron beam for other complementary experimens”, DONES-PreP WP8.2-2
A. Letourneau, “Report on the complementary experiments with neutrons”, DONES-PreP WP8.1-1
F. Arbeiter, “Catalogue of posible irradiaton modules for DONES”, DONES-PreP WP8.3-1
F. Arbeiter, “Report on conceptual design of other irradiation modules for DONES” DONES-PreP WP8.3-2
M. Vázquez, C. Torregrosa, F. Martín-Fuertes, J. C. Marugán, “Identification of Complementary Experiments in R160 and preliminary safety implications”
M. Vázquez, C. Torregrosa, F. Martín-Fuertes, J. C. Marugán, “Identification of Complementary Experiments in R026 and preliminary safety implications”
A. Maj, N. Harrakeh, M. Lewitowicz, W. Krolas, A. Ibarra, “White Book on the Complementary Scientifique Programme at IFMIF-DONES”, Krakow, November 2016

## Slide 22: Thank you for your attention
S. Becerril; J. Castellanos | 2nd IFMIF_DONES Users Conference | 19th October 2023

## Slide 23
Main beam  D+ ion beam 125 mA / 40 MeV (5 MW) @ 175 MHz (CW, 5.7 ns period)
Single bunch extraction
  Extraction of a fraction (0.1 - 1%) of the beam @ 40 MeV
  For 0.1% case
    125 µA (averaged current)
    40 MeV
    175 kHz
    5 kW (averaged power)
  Bunch length < 10 ns
Slow extraction (whole beam)
  Based on a switching dipole solution
  Fastest chopper field switch = 50 ms
R026 – D+ Beam extraction modes
Example of bunch timing conditions (Single bunch)
Bunch extracted
1.8 ns
T = 5.7 ns
T = 3.9 ns
Shortest time to restore normal operation = 100 ms
Chopper activation every 10 s for 1% usage