## Slide 1
Preliminary Safety Assessments of IFMIF-DONES for Users and Experimental Proposals
2nd DONES Users Workshop 19/10/2023
Claudio Torregrosa
F. Martin-Fuertes, J.C Marugan, M. Vázquez and IFMIF-DONES Safety Team

## Slide 2: Outline
Introduction: Top Level Regulation Framework
Activity Permits & Operational Permits Schedule, Documentation, Safety Analysis Report
Complementary Experiment (CE) Proposals (R026, R160, TC)
Some Safety Implications of the Complementary Experiments
Safety Integration of CE within IFMIF-DONES Safety Design
Conclusions and some Take-home Hints 
1
2
3
4
5
6

## Slide 3: INTRODUCTION: Top-level Regulation Framework
IFMIF-DONES will be a 1st Category Radioactive Facility
In accordance with the Royal Decree 1836/1999, point 3 of Article 34.2(b) “Complex facilities in which very high inventories of radioactive substances are handled or beams of very high-energy radiation are produced, making the potential radiological impact of the facility significant“
It does not belong to "Nuclear Facility" classification
In accordance with Royal Decree 1836/1999 Art 11. Nuclear Installations are:
  Nuclear Power Plants
  Nuclear Reactors
  Nuclear Fuel Manufacturing Facilities
  Nuclear Waste Storage Facility
  Fission or Fusion Facilities or Devices

## Slide 4: Types of Permits Required for IFMIF-DOMES
Construction Permits
Activity Permits (non-radiological, Industrial Safety)
Operation Permits (radiological)
Issued by the local and regional authorities after submission of the corresponding Documentation
Issued by the local and regional authorities after submission of the corresponding Documentation
Issued by the Ministry (MITECO) after authorization by the Regulatory Body (CSN)
Needed to start Operation with Radiological Implications
Relevant for the Complementary Experiments

## Slide 5: Activity Permits (non-radiological, Industrial Safety)
Once the Construction of the Main and Auxiliary buildings are being finished, Activity Permits (Licencia de Uso) shall be requested to the Escúzar City Hall.
The requested Documentation is (among others):
  Final Construction Project
  Report of Activities and Non-Radiological Safety Assessments
  Certificates of conformance with the regulations issued by the regional Government (Junta Andalucía), such as:
    Pressurized Equipment’s Regulation
    Regulations of Machinery/Cranes..
    Acoustic Protections Regulation
    Low/medium Voltage Regulation
    Fire Protection Regulations
    Thermal Installations in buildings Regulation
    ...Other Applicable Harmonized Regulations
Designs following the corresponding Spanish and European
Harmonised Standards
Documentation and Quality Plans will be delivered to the local and regional administrations to obtain the
“Activity Permits”

## Slide 6: Operation Permits – Gradual Strategy
Gradual Strategy, based on Temporary Permits until the Full-Permit is Granted, consistent with the Commissioning Phases of the Facility
PHASE I -> Injector + Low Power Beam Dump
PHASE II -> Injector + RFQ + Low Power Beam Dump
PHASE IV-> Full Facility
(Accelerator + Target Li loop + Irradiation Modules)
PHASE III -> Accelerator + High Power beam Dump (Pulse mode)
2nd Category Radioactive Installation
(Temporary Permits)
1st Category Radioactive Installation
Relevant for the Complementary Experiments

## Slide 7: Licensing Timeline
Project Milestones
Licensing Milestones
Start
Construction Sites and Main Building
Start Phase II
Commissioning
Start Phase I
Commissioning
Start Phase III
Start Phase IV
(Full Facility)
Granted pre-OP Phase I
2024
2025
2026
2027
2028
2030
2031
2029
2032
Finish
Construction Main Building and Services
Construction License
Granted
Construction License Request
Request OP Phase I
Request OP Phase II
Granted pre-OP Phase III
Request OP Phase III
Granted pre-OP Phase II
Request OP
Phase IV Full-Facility
Granted Pre-Op
Phase IV Full Facility
Activity Licenses Requests and Grantings
Some important dates for Complementary Experiments with Significant Safety Implications
Request of Phase IV Operational License in 2029
To be granted by 2032
Most relevant key Safety Information of Complementary Experiments with significant Safety Implications in the Licensing and Safety Design shall be provided years in advance 2029, to be integrated in the Safety files and Op. Licence Request

## Slide 8: Operation Permits (Radiological) – Documentation
Documentation Required for Category I Radioactive Facility Operation Authorization (RD 1836/1999):
Descriptive Report of the facility (including site and surrounding land)
Safety Analysis Report
Verification of the facility (Compliance tests and documentation including maintenance & periodic inspection plans)
Operating Rules. Including:
  Quality Assurance Manual
  Radiation Protection Manual
  Technical Specifications of Plant operation (Performance Tech. Specifications)
Internal Emergency Plan
Provisions for closure and financial coverage
Economic budget of the investment to be made
Physical Protection Plan (Security)

## Slide 9: Safety Analysis Report
  General Description of the Facility
  Main Design Criteria
  Design Basis of the Facility
  Conduct of Operation
  Protection Against Radiation and Waste Management
  Accident Analyses
  Safety Requirements
  ...
Safety Analysis Report (SAR) -> Reference Document in continuous Update
#41 Reference Accident Scenarios Identified and Analysed
Deterministic Analysis
/Reduction of conservative uncertainties
Definition of Safety Requirements, Safety Important Components, and Confinement

## Slide 10: Outline
Introduction: Top Level Regulation Framework and Procedures
Activity Permits & Operational Permits Schedule, Documentation, Safety Analysis Report
Complementary Experiment (CE) Proposals (R026, R, TC)
Some Safety Implications of the Complementary Experiments
Safety Integration of CE within IFMIF-DONES Safety Design
Conclusions
1
2
3
4
5
6

## Slide 11: Areas of Complementary Experiments
R160
R160:
Same floor as the Test Cell
Profiting from a continuous neutron beam from the TC via a Neutron Beam Aperture/Collimator (Ø20-12 cm)
Room of 26.6 m x 11.25 m (300 m2).
Estimated neutron flux at the duct exit:
2∙10¹⁰ n/cm²/s, 99.5% of fast neutrons, En > 100 keV
R026:
Ground floor, below the Accelerator Vault
Profiting from Pulsed Deuterons beams via a beam extraction from the accelerator
Room of 60 m x 36 m.
Deuteron extraction at 40 MeV (1 % intensity)
Experiment using deuterons & pulsed neutrons (by neutron production with a Target)
In the Test Cell:
High flux Modules
Medium Flux Modules
Low Flux Modules

## Slide 12: Preliminary List of Potential Experiment Proposals
R160
1) Fundamental particle physics studies with cold and ultra-cold neutrons.
2) Neutron scattering experiments with moderated beams:
3) Experiments with samples exposed to neutrons:
Activation of small samples by neutrons
Characterization of materials by radiation analysis
Neutron imaging
Fast neutron irradiation of components, devices or bio-samples
4) Medical treatment of patients using neutrons. BNCT
R026
1) Experiments using Pulsed Deuterons Beams
Production of radionuclides with intense deuteron beams
Deuteron-induced reactions
2) Experiments using Pulsed Neutron Beams (nTOF):
Neutron Cross-section measurements
Gamma-spectroscopy of the nuclei produced in fast-neutron-induced fission reaction
Half-life measurements of long-lived isotopes
Test Cell
1) Experiments Irradiating Material Specimens
Creep Fatigue Test Module (CFTM)
2) Experiments Irradiating Components
Activated Corrosion Product Test Module (ACPTM)
Irradiation of Instruments and Diagnostics
In-situ Ceramic Breeder Test Module
3) Experiments on Tritium Breeders Materials
Ceramic breeders
Lithium breeders
4) Radioisotopes Production

## Slide 13
Introduction: Top Level Regulation Framework and Procedures
Activity Permits & Operational Permits Schedule, Documentation, Safety Analysis Report
Complementary Experiment (CE) Proposals (R026, R, TC)
Some Safety Implications of the Complementary Experiments
Safety Integration of CE within IFMIF-DONES Safety Design
Conclusions
1
2
3
4
5
6

## Slide 14: Some Safety Implications that shall be considered
Radioactive Inventory and Contribution to Material at Risk
Impact of the Experimental Setups to eventual Reference Accidents Scenarios -> Definition of Safety-credited components for prevention/detection/mitigation (applicable)
Radioprotection Aspects
Industrial-Conventional Safety (non-radiological)

## Slide 15: Radioactive Inventory and contribution to Material at Risk
Particularly relevant for Tritium Breeders, Radioisotopes Production and non-encapsulated samples of actinides.
For the case of Tritium Breeders or Radioisotope Production, it could influence some design decisions regarding overall Safety Strategy and Experiments Designs.
Example:
Tritium Ceramic Breeders:
Assuming a tritium production of 6.35∙1011 atoms-T/g-CB/s
Leads to an activity production of 1.13∙103 Bq/g-CB/s
If we have a “Tritium Activity Budget” inside the TC in the order of 50 TBq (RCC-MRx Class 3)
This leads to 1 year irradiation of max of 2 kg of Ceramic Breeder Material
We could be producing 0.14 g of Tritium per year.
Total MAR inventory of IFMIF-DONES is 2340 TBq.
Ceramic Breeding contribute only to 2 % of total inventory
Just Very rough estimations!
Is this compatible with the Breeders Research Needs?
Let´s Iterate!

## Slide 16
Neutron Production Target/Converter
Beam windows:
Control of the extracted deuteron beam power. (risk of damage the downstream window/neutron production target in case of over-intensity extraction).
Safety/MP aspects related to extraction fail and beam impact of the vacuum chambers. (prompted dose)
Contribution air inrush RAS
Deuteron Beam Extraction Line: (5 kW extraction)
Neutron beam line to the R160 (shutter)
R160 Neutron Beam Dump
Tritium Breeders Modules Failure: (Tritium leaks)
Radioisotopes Modules / Process Failure:
Impact of Complementary Experiments on RAS?

## Slide 17: Radioprotection Aspects
Key Information:
  Access of Personnel and Intervention times in Complementary Experimental Areas. Maintenance?
  Contribution to Occupational Radiation Exposure ORE)
  Operational Modes, Activation and Prompt Radiation to adjacent Areas
    Will it be necessary to have additional shielding?
    Risk of Contamination?
    How the experimental setups assemblies will be activated?, preference of using low activation materials..
  Management of Radioactive Waste and Decommissioning of the Experimental Setups

## Slide 18: Industrial-Conventional (non-radiological) Safety
Examples:
Cryogenics
Gaseous releases
  Oxygen Deficiency Hazard (ODH)
  Explosive gases?
Pressurized Equipment
Machinery
Fire hazards
Electric hazards
Cold Moderator
Liquid CH4
Liquid H2
BeO
Designs must follow the corresponding Spanish and European
Harmonised Standards

## Slide 19
Introduction: Top Level Regulation Framework and Procedures
Activity Permits & Operational Permits Schedule, Documentation, Safety Analysis Report
Complementary Experiment (CE) Proposals (R026, R, TC)
Some Safety Implications of the Complementary Experiments
Safety Integration of CE within IFMIF-DONES Safety Design
Conclusions
1
2
3
4
5
6

## Slide 20: IFMIF-DONES Confinement Barriers
Complementary Experiments in R160 and R026 will be inside the HVAC-Dynamic Confinement Barrier
Complementary Experiments in the Test Cell. Inside the 1st Safety TC/LLC/TIR Barrier (Metallic Liner)
Any pipe-penetration that may be required through the liner in the
TC-complementary experiments shall be equipped with Safety-Credited Isolation Valves

## Slide 21: Safety Control System-Plant Safety Subsystem (SCS-PSS)
18 Safety Commands (Actuations)
31 Safety Interlocks (Instruments)
Control Logics to bring the Facility to "Plant-Safe-State"
Complementary Experiments that may require Safety-credited Instrumentation and the actuation of Safety Interlock Commands (i.e. Beam Safety Shutdown) shall integrate them within the SCS-Plant Safety System

## Slide 22: PASS and RAMSES
Personal Access Safety subsystem (PASS):
“Personal Access Interlock Subsystem.”
  In access mode: no beam or hazard in the zone;
  In beam mode: no personnel in the zone and the beam shall be stopped immediately in case of an intrusion.
RAdiation Monitoring Subsystem for the Environment and Safety (RAMSES)
CERN’s CROME
CERN’s PS Access System
Very Relevant for the Complementary Experiments in which Access to Experimental Rooms will be necessary while the Facility is in Operation Mode
Interfaces with the Complementary Experimental Areas. Also, in case of eventual needs of cooling systems with potential coolant activation.

## Slide 23
Introduction: Top Level Regulation Framework and Procedures
Activity Permits & Operational Permits Schedule, Documentation, Safety Analysis Report
Complementary Experiment (CE) Proposals (R026, R160, TC)
Some Safety Implications of the Complementary Experiments
Safety Integration of CE within IFMIF-DONES Safety Design
Conclusions and some Take-home Hints 
1
2
3
4
5
6

## Slide 24: Conclusions and Take-home Hints
Complementary Experiments, as part of the IFMIF-DONES Facility, shall be well integrated within its Safety Requirements.
While the extremely interesting and valuable Experimental Proposals are made and the designs are maturing, please, take also in mind Safety Aspects and Implications and gather this information. Some of it:
  Material at Risk (i.e. mobilizable inventory)
  Possible Contribution to Reference Accidents Scenarios
  Radioprotection Aspects (Operation modes, activation, intervention times, etc.)
  Industrial Safety (non-radiological)
The earlier interaction with the Safety Team and inclusion of Safety Assessments in the Experiment Proposals the better for the implementation success!
We remain fully-available to any question and pursuing valuable feedback to be integrated in this iterative process.
Safety
Experiment Proposals and Designs

## Slide 25
Thanks very much!!
Questions?