## Slide 1: Possible experiments at DONES with pulsed deuteron beams
Bogdan Fornal, Łukasz Iskra (IFJ PAN) + contribution from the fnuc @ DONES working group
Presented by
Adam Maj (IFJ PAN Krakow)
This work has been carried out within the framework of the EUROfusion Consortium, funded by the European Union via the Euratom Research and Training Programme (Grant Agreement No 101052200 — EUROfusion). Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Commission. Neither the European Union nor the European Commission can be held responsible for them.am
Second DONES Users Workshop
October 19-20, 2023, Granada

## Slide 2
(A. Maj)

## Slide 3
Experimental area
~40 m
~80 m
1/1000 fraction of 40-MeV deuterons
7.6 ns pulses
5.7 µs repetition time

## Slide 4
1. Experiments using pulsed deutrons
1.1. Deuteron-induced reactions
1.2. Radionuclides production
44Ca (d,2n) 44Sc
64Ni (d,2n) 64Cu
(d,6Li) type – alpha pick-up
(d,3He) type – proton pick-up
(d,p) type – neutron transfer
(d,t) type – neutron pick-up
186W(d,2n)186Re
2. Experiments using secondary (induced
by deuterons) pulsed beam of neutrons
2.2. Investigation of pygmy dipole resonances
2.1. Neutron-induced fission
238U(n,f), 232Th(n,f), 230Th, 226Ra, …
2.3. Half-life measurements of long-lived isotopes
2.4. Neutron-induced reaction cross section
measurements in a wide neutron energy range.
Neutron Time-of-Flight Facility

## Slide 5
(d,6Li) type – alpha pick-up
(d,3He) type – proton pick-up
(d,p) type – neutron transfer
(d,t) type – neutron pick-up
1.1. Deuteron-induced reactions
detailed investigations of the decay of isomeric states in products of the reactions induced by deuterons on different stable and radioactive targets

## Slide 6
1.2. Radionuclides production
186W(d,2n)186Re
With deuterons production yield five times higher than with protons.
186W(p,n)186Re
186W(d,2n)186Re
44Ca (d,2n) 44Sc

## Slide 7
neutron converter
deuterons
neutrons
shielding
target
detector systems
Experiments using secondary (induced by deuterons)
pulsed beam of neutrons

## Slide 8
Deuteron-neutron convertion - Monte Carlo simulations
High nominal intensity in the 5 to 30 MeV neutron energy range
Excellent energy resolution
Various beam lines available with the potential of performing various experiments at the same time

## Slide 9
2.1. Fast-neutron-induced fission – gamma-ray spectroscopy of exotic products
238U(n,f), 232Th(n,f), 230Th, 226Ra, …

## Slide 10
Occurence of microsecond isomers
in the known nuclei
Neutron number
Proton number
208Pb
78Ni
132Sn
expected low-lying high-spin isomers
- candidates for neutron-radioactivity

## Slide 11
Spontaneous fission of 248Cm
Thermal neutron induced fission
of 235U
Yields of products
from the 14 MeV-neutron
induced fission of 232Th
n(14 MeV) + 232Th
232Th
226Ra
230Th
?
235U
Fast-neutron-induced fission
of radioactive targets 230Th, 226Ra

## Slide 12
28
36
38
30
34
40
32
Ga
Zn
Ge
Ni
Cr
Fe
Ti
V
Mn
Co
Cu
As
Se
Br
Kr
Rb
42
44
46
48
70Zn
50
78Ni
Yields of products from neutron
induced fission in the region
of interest
n(therm) + 235U
n(14 MeV) + 232Th

## Slide 13
Gas-filled compact magnetic spectrometer
(the idea comes from ILL Grenoble where such spectrometer is being constructed)
neutron
beam
Ge array
at focal plane
Ge array around
target
target

## Slide 14
„Left” fragment stopped in the backing
→ Doppler free prompt γ detection
target
target
material
backing
„Right” fragment will fly to the spectrometer
→ A, Z determination; delayed γ spectroscopy
coincidences
fission product
toward
spectrometer
Fast-neutron-induced fission on light actinide targets

## Slide 15
2.2. Investigation of pygmy dipole resonances
- synergy with the proposed experiments at NSF GANIL
DONES-IFMIF facility, providing a high-intensity neutron beam (with energies up to ~40 MeV) and 40-MeV deuteron beam, will be an ideal for such measurements.
E* [MeV]
PDR
IV GDR
IS GQR
15
0
Bn≈8
So far, investigations of Pygmy Dipole resonance were carried out using
the (g, g’), (p, p’), (a, a’) and (HI, HI’) inelastic scattering experiments.
Adding new probes, as neutron or deuteron, will allow to shed new light
on the origin of the PDR excitations.

## Slide 16
2.2. Neutron-induced reaction cross section measurements
(on stable and radioactive targets)
in a wide neutron energy range.

## Slide 17
2.4. Toward Neutron Time-of-Flight Facility?
Neutron converter
deuterons
neutrons

## Slide 18
The Spanish nuclear physics network fnuc has promoted a study group for exploring the nuclear physics opportunities at DONES.
Coordinators: Daniel Cano-Ott (CIEMAT), Antonio Lallena (Univ. Granada)
WP1. Facility and simulations (E. Mendoza – CIEMAT)
WP2. Fundamental nuclear physics (C. Guerrero – Univ. Sevilla)
WP3. Applications (C. Domingo – IFIC)
Willingness to establish a close collaboration with the preparatory phase WPs working on the same activities!
Neutron Time-of-Flight facility based on a neutron-pulsed beam produced with 40-MeV deuterons ?
The fnuc @ DONES working group

## Slide 19
1. Experiments using pulsed deutrons
1.1. Deuteron-induced reactions
1.2. Radionuclides production
44Ca (d,2n) 44Sc
64Ni (d,2n) 64Cu
(d,6Li) type – alpha pick-up
(d,3He) type – proton pick-up
(d,p) type – neutron transfer
(d,t) type – neutron pick-up
186W(d,2n)186Re
2. Experiments using secondary (induced
by deuterons) pulsed beam of neutrons
2.2. Investigation of pygmy dipole resonances
2.1. Neutron-induced fission
238U(n,f), 232Th(n,f), 230Th, 226Ra, …
2.3. Half-life measurements of long-lived isotopes
2.4. Neutron-induced reaction cross section
measurements in a wide neutron energy range.
Neutron Time-of-Flight Facility
Summary
Exceptional opportunities at DONES for the advanced world leading nuclear physics investigations
Ł.W. Iskra, B. Fornal, D. Cano-Ott, E. Mendoza et al., „Report on possible complementary experiments to be developed in DONES using deuterons” https://idm.dones.irb.hr/op/op.ViewOnline.php?documentid=244&version=1